## Slide 1
Events
FlameDetection: Rising edge on GPIO connected to Flame Sensor (x4), when a flame is detected on any of the sensors.
DataReady ADC: Rising edge on GPIO connected to Data Ready pin on ADC integrated circuit once a new analogue measurement is ready.
Timers
Ultrasonic sensor : Trigger the sensor measurement periodically in pseudo blocking timer

## Slide 2: Flame distance idea
θ
a
b
Starting from the assumption of having a very narrow angle of detection in the sensors; We can set two sensors at a known distance a from each other and with a known angle θ from the horizontal axis.
If we position the robot in an orientation in which both sensors measure the flame with the same intensity, we may assume we are b distance apart from the flame source.

## Slide 3
However, the IR sensor has a detection angle of 60°. That means that we will have a range of distance detection.
Still, we won’t be able to know the exact distance, but at least that we are within certain range.
Considerations:
I think we will need to have two sets of flame sensors. One with at least 3 sensors to detect the direction of the flame source. And a second one with this configuration.
This way, the robot can scan the surroundings until it finds the flame and once the robot is positioned in the right orientation it can start to approach the flame until the source is within the range of the second set of sensors.